## Slide 1
Chapter 7:
Microarchitecture
Digital Design &
Computer Architecture
Sarah Harris & David Harris

## Slide 2
Chapter 7 :: Topics
Introduction
Performance Analysis
Single-Cycle Processor
Multicycle Processor
Pipelined Processor
Advanced Microarchitecture

## Slide 3
Introduction
Microarchitecture: how to implement an architecture in hardware
Processor:
  Datapath: functional blocks
  Control: control signals

## Slide 4
Microarchitecture
Multiple implementations for a single architecture:
  Single-cycle: Each instruction executes in a single cycle
  Multicycle: Each instruction is broken up into series of shorter steps
  Pipelined: Each instruction broken up into series of steps & multiple instructions execute at once

## Slide 5
Processor Performance
Program execution time
Execution Time = (#instructions)(cycles/instruction)(seconds/cycle)
Definitions:
  CPI: Cycles/instruction
  clock period: seconds/cycle
  IPC: instructions/cycle = IPC
Challenge is to satisfy constraints of:
  Cost
  Power
  Performance

## Slide 6
RISC-V Processor
Consider subset of RISC-V instructions:
  R-type ALU instructions:
    add, sub, and, or, slt
  Memory instructions:
    lw, sw
  Branch instructions:
    beq

## Slide 7
Architectural State Elements
Determines everything about a processor:
  Architectural state:
    32 registers
    PC
    Memory

## Slide 8
RISC-V Architectural State Elements

## Slide 9
Chapter 7: Microarchitecture
Single-Cycle
RISC-V Processor

## Slide 10
Single-Cycle RISC-V Processor
Datapath
Control

## Slide 11
Example Program
Design datapath
View example program executing
Example Program:

## Slide 12
Single-Cycle RISC-V Processor
Datapath: start with lw instruction
Example: lw x6, -4(x9)
lw rd, imm(rs1)

## Slide 13
Single-Cycle Datapath: lw fetch
STEP 1: Fetch instruction

## Slide 14
Single-Cycle Datapath: lw Reg Read
STEP 2: Read source operand (rs1) from RF

## Slide 15
Single-Cycle Datapath: lw Immediate
STEP 3: Extend the immediate

## Slide 16
Single-Cycle Datapath: lw Address
STEP 4: Compute the memory address
ALUControl2:0 | Function
000 | add
001 | subtract
010 | and
011 | or
101 | SLT

## Slide 17
Single-Cycle Datapath: lw Mem Read
STEP 5: Read data from memory and write it back to register file

## Slide 18
Single-Cycle Datapath: PC Increment
STEP 6: Determine address of next instruction

## Slide 19
Chapter 7: Microarchitecture
Single-Cycle
Datapath: Other Instructions

## Slide 20
Single-Cycle Datapath: sw
Immediate: now in {instr[31:25], instr[11:7]}
Add control signals: ImmSrc, MemWrite

## Slide 21
Single-Cycle Datapath: Immediate
ImmSrc | ImmExt | Instruction Type
0 | {{20{instr[31]}}, instr[31:20]} | I-Type
1 | {{20{instr[31]}}, instr[31:25], instr[11:7]} | S-Type

## Slide 22
Single-Cycle Datapath: R-type
Read from rs1 and rs2 (instead of imm)
Write ALUResult to rd

## Slide 23
Single-Cycle Datapath: beq
Calculate target address: PCTarget = PC + imm

## Slide 24
Single-Cycle Datapath: ImmExt
ImmSrc1:0 | ImmExt | Instruction Type
00 | {{20{instr[31]}}, instr[31:20]} | I-Type
01 | {{20{instr[31]}}, instr[31:25], instr[11:7]} | S-Type
10 | {{19{instr[31]}}, instr[31], instr[7], instr[30:25], instr[11:8], 1’b0} | B-Type

## Slide 25
Single-Cycle RISC-V Processor

## Slide 26
Chapter 7: Microarchitecture
Single-Cycle
Control

## Slide 27
Single-Cycle Control
High-Level View
Low-Level View

## Slide 28
Single-Cycle Control: Main Decoder
op | Instr. | RegWrite | ImmSrc | ALUSrc | MemWrite | ResultSrc | Branch | ALUOp
3 | lw | 1 | 00 | 1 | 0 | 1 | 0 | 00
35 | sw | 0 | 01 | 1 | 1 | X | 0 | 00
51 | R-type | 1 | XX | 0 | 0 | 0 | 0 | 10
99 | beq | 0 | 10 | 0 | 0 | X | 1 | 01

## Slide 29
Review: ALU
ALUControl2:0 | Function
000 | add
001 | subtract
010 | and
011 | or
101 | SLT

## Slide 30
Review: ALU
ALUControl2:0 | Function
000 | add
001 | subtract
010 | and
011 | or
101 | SLT

## Slide 31
Review: ALU with Overflow Detection
ALUControl2:0 | Function
000 | add
001 | subtract
010 | and
011 | or
101 | SLT

## Slide 32
Single-Cycle Control: ALU Decoder

## Slide 33
Single-Cycle Control: ALU Decoder
ALUOp | funct3 | op5 , funct75 | Instruction | ALUControl2:0
00 | x | x | lw, sw | 000 (add)
01 | x | x | beq | 001 (subtract)
10 | 000 | 00, 01, 10 | add | 000 (add)
 | 000 | 11 | sub | 001 (subtract)
 | 010 | x | slt | 101 (set less than)
 | 110 | x | or | 011 (or)
 | 111 | x | and | 010 (and)

## Slide 34
Example: and
op | Instruct | RegWrite | ImmSrc | ALUSrc | MemWrite | ResultSrc | Branch | ALUOp
51 | R-type | 1 | XX | 0 | 0 | 0 | 0 | 10
and x5, x6, x7

## Slide 35
Chapter 7: Microarchitecture
Extending the
Single-Cycle
Processor

## Slide 36
Extended Functionality: I-Type ALU
Enhance the single-cycle processor to handle I-Type ALU instructions: addi, andi, ori, and slti
Similar to R-type instructions
But second source comes from immediate
Change ALUSrc to select the immediate
And ImmSrc to pick the correct immediate

## Slide 37
Extended Functionality: I-Type ALU
op | Instruct. | RegWrite | ImmSrc | ALUSrc | MemWrite | ResultSrc | Branch | ALUOp
3 | lw | 1 | 00 | 1 | 0 | 1 | 0 | 00
35 | sw | 0 | 01 | 1 | 1 | X | 0 | 00
51 | R-type | 1 | XX | 0 | 0 | 0 | 0 | 10
99 | beq | 0 | 10 | 0 | 0 | X | 1 | 01
19 | I-type | 1 | 00 | 1 | 0 | 0 | 0 | 10

## Slide 38
Extended Functionality: addi
op | Instruct. | RegWrite | ImmSrc | ALUSrc | MemWrite | ResultSrc | Branch | ALUOp
19 | I-type | 1 | 00 | 1 | 0 | 0 | 0 | 10
addi x5, x6, -33

## Slide 39
Extended Functionality: jal
Enhance the single-cycle processor to handle jal
Similar to beq
But jump is always taken
  PCSrc should be 1
Immediate format is different
  Need a new ImmSrc of 11
And jal must compute PC+4 and store in rd
  Take PC+4 from adder through ResultMux

## Slide 40
Extended Functionality: jal

## Slide 41
Extended Functionality: ImmExt
ImmSrc1:0 | ImmExt | Instruction Type
00 | {{20{instr[31]}}, instr[31:20]} | I-Type
01 | {{20{instr[31]}}, instr[31:25], instr[11:7]} | S-Type
10 | {{19{instr[31]}}, instr[31], instr[7], instr[30:25], instr[11:8], 1’b0} | B-Type
11 | {{12{instr[31]}}, instr[19:12], instr[20], instr[30:21], 1’b0} | J-Type

## Slide 42
Extended Functionality: jal
op | Instruct. | RegWrite | ImmSrc | ALUSrc | MemWrite | ResultSrc | Branch | ALUOp | Jump
3 | lw | 1 | 00 | 1 | 0 | 01 | 0 | 00 | 0
35 | sw | 0 | 01 | 1 | 1 | XX | 0 | 00 | 0
51 | R-type | 1 | XX | 0 | 0 | 00 | 0 | 10 | 0
99 | beq | 0 | 10 | 0 | 0 | XX | 1 | 01 | 0
19 | I-type | 1 | 00 | 1 | 0 | 00 | 0 | 10 | 0
111 | jal | 1 | 11 | X | 0 | 10 | 0 | XX | 1

## Slide 43
Extended Functionality: jal
op | Instruct. | RegWrite | ImmSrc | ALUSrc | MemWrite | ResultSrc | Branch | ALUOp | Jump
111 | jal | 1 | 11 | X | 0 | 10 | 0 | XX | 1

## Slide 44
Chapter 7: Microarchitecture
Single-Cycle
Performance

## Slide 45
Processor Performance
Program Execution Time
= (#instructions)(cycles/instruction)(seconds/cycle)
= # instructions x CPI x TC

## Slide 46
Single-Cycle Processor Performance
TC limited by critical path (lw)

## Slide 47
Single-Cycle Processor Performance
Single-cycle critical path:
Tc_single = tpcq_PC + tmem + max[tRFread, tdec + text + tmux] + tALU + tmem + tmux + tRFsetup
Typically, limiting paths are:
  memory, ALU, register file
  So, Tc_single = tpcq_PC + tmem + tRFread + tALU + tmem + tmux + tRFsetup
  = tpcq_PC + 2tmem+ tRFread + tALU + tmux + tRFsetup

## Slide 48
Single-Cycle Performance Example
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 40
Register setup | tsetup | 50
Multiplexer | tmux | 30
AND-OR gate | tAND-OR | 20
ALU | tALU | 120
Decoder (Control Unit) | tdec | 25
Extend unit | text | 35
Memory read | tmem | 200
Register file read | tRFread | 100
Register file setup | tRFsetup | 60
  = (40 + 2*200 + 100 + 120 + 30 + 60) ps = 750 ps
  Tc_single = tpcq_PC + 2tmem + tRFread + tALU + tmux + tRFsetup

## Slide 49
Single-Cycle Performance Example
Program with 100 billion instructions:
Execution Time = # instructions x CPI x TC
= (100 × 109)(1)(750 × 10-12 s)
= 75 seconds

## Slide 50
Chapter 7: Microarchitecture
Multicycle RISC-V Processor

## Slide 51
Single- vs. Multicycle Processor
Single-cycle:
  + simple
  cycle time limited by longest instruction (lw)
  separate memories for instruction and data
  3 adders/ALUs
Multicycle processor addresses these issues by breaking instruction into shorter steps
  shorter instructions take fewer steps
  can re-use hardware
  cycle time is faster

## Slide 52
Single- vs. Multicycle Processor
Single-cycle:
  + simple
  cycle time limited by longest instruction (lw)
  separate memories for instruction and data
  3 adders/ALUs
Multicycle:
  + higher clock speed
  + simpler instructions run faster
  + reuse expensive hardware on multiple cycles
  - sequencing overhead paid many times
Same design steps as single-cycle:
first datapath
then control

## Slide 53
Multicycle State Elements
Replace separate Instruction and Data memories with a single unified memory – more realistic

## Slide 54
Multicycle Datapath: Instruction Fetch
STEP 1: Fetch instruction

## Slide 55
Multicycle Datapath: lw Get Sources
STEP 2: Read source operand from RF and extend immediate

## Slide 56
Multicycle Datapath: lw Address
STEP 3: Compute the memory address

## Slide 57
Multicycle Datapath: lw Memory Read
STEP 4: Read data from memory

## Slide 58
Multicycle Datapath: lw Write Register
STEP 5: Write data back to register file

## Slide 59
Multicycle Datapath: Increment PC
STEP 6: Increment PC: PC = PC+4

## Slide 60
Chapter 7: Microarchitecture
Multicycle Datapath: Other Instructions

## Slide 61
Multicycle Datapath: sw
Write data in rs2 to memory

## Slide 62
Multicycle Datapath: beq
Calculate branch target address:
BTA = PC + imm
PC is updated in Fetch stage, so need to save old (current) PC

## Slide 63
Multicycle RISC-V Processor

## Slide 64
Chapter 7: Microarchitecture
Multicycle Control

## Slide 65
Multicycle Control
High-Level View
Low-Level View
ALU Decoder same as single-cycle

## Slide 66
Multicycle Control: Instruction Decoder
op | Instruction | ImmSrc
3 | lw | 00
35 | sw | 01
51 | R-type | XX
99 | beq | 10

## Slide 67
Multicycle Control: Main FSM
To declutter FSM:
Write enable signals (RegWrite, MemWrite, IRWrite, PCUpdate, and Branch) are 0 if not listed in a state.
Other signals are don’t care if not listed in a state

## Slide 68
Main FSM: Fetch

## Slide 69
Main FSM: Decode
Recall that ImmSrc is determined by the Instruction Decoder

## Slide 70
Main FSM: Address

## Slide 71
Main FSM: Read Memory

## Slide 72
Main FSM: Read Memory Datapath

## Slide 73
Main FSM: Write RF

## Slide 74
Main FSM: Write RF Datapath

## Slide 75
Main FSM: Fetch Revisited
Calculate PC+4 during Fetch stage (ALU isn’t being used)

## Slide 76
Main FSM: Fetch (PC+4) Datapath
Fetch Instruction and
Increment PC

## Slide 77
Chapter 7: Microarchitecture
Multicycle Control: Other Instructions

## Slide 78
Main FSM: sw

## Slide 79
Main FSM: sw Datapath

## Slide 80
Main FSM: R-Type Execute

## Slide 81
Main FSM: R-Type Execute Datapath

## Slide 82
Main FSM: R-Type ALU Write Back

## Slide 83
Main FSM: R-Type ALU Write Back

## Slide 84
Main FSM: beq
Need to calculate:
  Branch Target Address
  rs1 - rs2 (to see if equal)
ALU isn’t being used in Decode stage
  Use it to calculate Target Address (PC + imm)

## Slide 85
Main FSM: Decode Revisited
Read Registers and
Calculate Target Address (PC+imm)

## Slide 86
Main FSM: Decode (Target Address)
Read Registers and
Calculate Target Address (PC+imm)

## Slide 87
Main FSM: beq

## Slide 88
Main FSM: beq Datapath
Compare registers and
Send Target PC (ALUOut) to PCNext

## Slide 89
Chapter 7: Microarchitecture
Extending the RISC-V Multicycle Processor

## Slide 90
Main FSM: I-Type ALU Execute

## Slide 91
Main FSM: I-Type ALU Exec. Datapath

## Slide 92
Main FSM: jal

## Slide 93
Main FSM: jal Datapath
Calculate PC + 4 and
Send Target Address (ALUOut) to PCNext

## Slide 94
Main FSM: jal
PC + 4 is written to rd in S7: ALUWB

## Slide 95
Multicycle Processor Main FSM

## Slide 96
Chapter 7: Microarchitecture
Multicycle Performance

## Slide 97
Multicycle Processor Performance
Instructions take different number of cycles:
  3 cycles: beq
  4 cycles: R-type, addi, sw , jal
  5 cycles: lw
CPI is weighted average
SPECINT2000 benchmark:
  25% loads
  10% stores
  13% branches
  52% R-type
Average CPI = (0.13)(3) + (0.52 + 0.10)(4) + (0.25)(5) = 4.12

## Slide 98
Multicycle Critical Path
Potential Critical Paths:
Calculate PC + 4 or
Read Memory

## Slide 99
Multicycle Processor Performance
Multicycle critical path:
Assumptions:
  RF is faster than memory
  Writing memory is faster than reading memory
Tc_multi = tpcq + tdec + 2tmux + max(tALU , tmem) + tsetup

## Slide 100
Multicycle Performance Example
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 40
Register setup | tsetup | 50
Multiplexer | tmux | 30
AND-OR gate | tAND-OR | 20
ALU | tALU | 120
Decoder (Control Unit) | tdec | 25
Extend unit | tdec | 35
Memory read | tmem | 200
Register file read | tRFread | 100
Register file setup | tRFsetup | 60
  = (40 + 25 + 2*30 + 200 + 50) ps = 375 ps
  Tc_multi = tpcq + tdec + 2tmux + max(tALU , tmem) + tsetup

## Slide 101
Multicycle Performance Example
For a program with 100 billion instructions executing on a multicycle RISC-V processor
  CPI = 4.12 cycles/instruction
  Clock cycle time: Tc_multi = 375 ps
Execution Time = (# instructions) × CPI × Tc
= (100 × 109)(4.12)(375 × 10-12)
= 155 seconds
This is slower than the single-cycle processor (75 sec.)
.

## Slide 102
Chapter 7: Microarchitecture
Pipelined RISC-V Processor

## Slide 103
Pipelined RISC-V Processor
Temporal parallelism
Divide single-cycle processor into 5 stages:
  Fetch
  Decode
  Execute
  Memory
  Writeback
Add pipeline registers between stages

## Slide 104
Single-Cycle vs. Pipelined Processor

## Slide 105
Pipelined Processor Abstraction

## Slide 106
Single-Cycle & Pipelined Datapaths
Signals in Pipelined Processor are appended with first letter of stage (i.e., PCF, PCD, PCE).

## Slide 107
Corrected Pipelined Datapath
Rd must arrive at same time as Result
Register file written on falling edge of CLK

## Slide 108
Pipelined Processor with Control
Same control unit as single-cycle processor
Control signals travel with the instruction (drop off when used)

## Slide 109
Chapter 7: Microarchitecture
Pipelined Processor Hazards

## Slide 110
Pipelined Hazards
When an instruction depends on result from instruction that hasn’t completed
Types:
  Data hazard: register value not yet written back to register file
  Control hazard: next instruction not decided yet (caused by branch)

## Slide 111
Data Hazard

## Slide 112
Handling Data Hazards
Insert nops in code at compile time
Rearrange code at compile time
Forward data at run time
Stall the processor at run time

## Slide 113
Handling Data Hazards
Insert enough nops for result to be ready
Or move independent useful instructions forward

## Slide 114
Data Forwarding
Data is available on internal busses before it is written back to the register file (RF).
Forward data from internal busses to Execute stage.

## Slide 115
Data Forwarding
Check if source register in Execute stage matches destination register of instruction in Memory or Writeback stage.
If so, forward result.

## Slide 116
Data Forwarding: Hazard Unit

## Slide 117
Data Forwarding
Case 1: Execute stage Rs1 or Rs2 matches Memory stage Rd?
Forward from Memory stage
Case 2: Execute stage Rs1 or Rs2 matches Writeback stage Rd?
Forward from Writeback stage
Case 3: Otherwise use value read from register file (as usual)
Equations for Rs1:
if ((Rs1E == RdM) AND RegWriteM) // Case 1
ForwardAE = 10
else if ((Rs1E == RdW) AND RegWriteW) // Case 2
ForwardAE = 01
else ForwardAE = 00 // Case 3
ForwardBE equations are similar (replace Rs1E with Rs2E)

## Slide 118
Data Forwarding
Case 1: Execute stage Rs1 or Rs2 matches Memory stage Rd?
Forward from Memory stage
Case 2: Execute stage Rs1 or Rs2 matches Writeback stage Rd?
Forward from Writeback stage
Case 3: Otherwise use value read from register file (as usual)
Equations for Rs1:
if ((Rs1E == RdM) AND RegWriteM) AND (Rs1E != 0) // Case 1
ForwardAE = 10
else if ((Rs1E == RdW) AND RegWriteW) AND (Rs1E != 0) // Case 2
ForwardAE = 01
else ForwardAE = 00 // Case 3
ForwardBE equations are similar (replace Rs1E with Rs2E)

## Slide 119
Data Hazard due to lw Dependency

## Slide 120
Stalling to solve lw Data Dependency

## Slide 121
Stalling Logic
Is either source register in the Decode stage the same as the destination register in the Execute stage?
AND
Is the instruction in the Execute stage a lw?
lwStall = ((Rs1D == RdE) OR (Rs2D == RdE)) AND ResultSrcE0
StallF = StallD = FlushE = lwStall
(Stall the Fetch and Decode stages, and flush the Execute stage.)

## Slide 122
Stalling Hardware

## Slide 123
Chapter 7: Microarchitecture
Pipelined Processor Control Hazards

## Slide 124
Control Hazards
beq:
  Branch not determined until the Execute stage of pipeline
  Instructions after branch fetched before branch occurs
  These 2 instructions must be flushed if branch happens

## Slide 125
Control Hazards
Branch misprediction penalty:
The number of instructions flushed when a branch is taken (in this case, 2 instructions)

## Slide 126
Control Hazards: Flushing Logic
If branch is taken in execute stage, need to flush the instructions in the Fetch and Decode stages
  Do this by clearing Decode and Execute Pipeline registers using FlushD and FlushE
Equations:
FlushD = PCSrcE
FlushE = lwStall OR PCSrcE

## Slide 127
Control Hazards: Flushing Hardware

## Slide 128
RISC-V Pipelined Processor with Hazard Unit

## Slide 129
Summary of Hazard Logic
Data hazard logic (shown for SrcA of ALU):
if ((Rs1E == RdM) AND RegWriteM) AND (Rs1E != 0) // Case 1
ForwardAE = 10
else if ((Rs1E == RdW) AND RegWriteW) AND (Rs1E != 0) // Case 2
ForwardAE = 01
else ForwardAE = 00 // Case 3
Load word stall logic:
lwStall = ((Rs1D == RdE) OR (Rs2D == RdE)) AND ResultSrcE0
StallF = StallD = lwStall
Control hazard flush:
FlushD = PCSrcE
FlushE = lwStall OR PCSrcE

## Slide 130
Chapter 7: Microarchitecture
Pipelined Performance

## Slide 131
Pipelined Processor Performance Example
SPECINT2000 benchmark:
  25% loads
  10% stores
  13% branches
  52% R-type
Suppose:
  40% of loads used by next instruction
  50% of branches mispredicted
What is the average CPI? (Ideally it’s 1, but…)
  Load CPI = 1 when not stalling, 2 when stalling
    So, CPIlw = 1(0.6) + 2(0.4) = 1.4
  Branch CPI = 1 when not stalling, 3 when stalling
  So, CPIbeq = 1(0.5) + 3(0.5) = 2
  Average CPI = (0.25)(1.4) + (0.1)(1) + (0.13)(2) + (0.52)(1) = 1.23

## Slide 132
Pipelined Processor Performance Example
Pipelined processor critical path:
Tc_pipelined = max of
tpcq + tmem + tsetup Fetch
2(tRFread + tsetup ) Decode
tpcq + 4tmux + tALU + tAND-OR + tsetup Execute
tpcq + tmem + tsetup Memory
2(tpcq + tmux + tRFwrite) Writeback
Decode and Writeback stages both use the register file in each cycle
So each stage gets half of the cycle time (Tc/2) to do their work
Or, stated a different way, 2x of their work must fit in a cycle (Tc)

## Slide 133
Pipelined Critical Path: Execute Stage

## Slide 134
Pipelined Performance Example
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 40
Register setup | tsetup | 50
Multiplexer | tmux | 30
AND-OR gate | tAND-OR | 20
ALU | tALU | 120
Decoder (Control Unit) | tdec | 25
Extend unit | tdec | 35
Memory read | tmem | 200
Register file read | tRFread | 100
Register file setup | tRFsetup | 60
  = (40 + 4*30 + 120 + 20 + 50) ps = 350 ps
  Tc_pipelined = tpcq + 4tmux + tALU + tAND-OR + tsetup

## Slide 135
Pipelined Performance Example
Program with 100 billion instructions
Execution Time = (# instructions) × CPI × Tc
= (100 × 109)(1.23)(350 × 10-12)
= 43 seconds

## Slide 136
Processor Performance Comparison
Processor | Execution Time (seconds) | Speedup (single-cycle as baseline)
Single-cycle | 75 | 1
Multicycle | 155 | 0.5
Pipelined | 43 | 1.7

## Slide 137
Chapter 7: Microarchitecture
Advanced Microarchitecture

## Slide 138
Advanced Microarchitecture
Deep Pipelining
Micro-operations
Branch Prediction
Superscalar Processors
Out of Order Processors
Register Renaming
SIMD
Multithreading
Multiprocessors

## Slide 139
Deep Pipelining
10-20 stages typical
Number of stages limited by:
  Pipeline hazards
  Sequencing overhead
  Power
  Cost

## Slide 140
Micro-operations
Decompose complex instructions into series of simple instructions called micro-operations (micro-ops or µ-ops)
At run-time, complex instructions are decoded into one or more micro-ops
Used heavily in CISC (complex instruction set computer) architectures (e.g., x86)
Complex Op Micro-op Sequence
lw s1, 0(s2), postincr 4 lw s1, 0(s2)
addi s2, s2, 4
Without μ-ops, would need 2nd write port on the register file

## Slide 141
Branch Prediction
Guess whether branch will be taken
  Backward branches are usually taken (loops)
  Consider history to improve guess
Good prediction reduces fraction of branches requiring a flush

## Slide 142
Branch Prediction
Ideal pipelined processor: CPI = 1
Branch misprediction increases CPI
Static branch prediction:
  Check direction of branch (forward or backward)
  If backward, predict taken
  Else, predict not taken
Dynamic branch prediction:
  Keep history of last several hundred (or thousand) branches in branch target buffer, record:
    Branch destination
    Whether branch was taken

## Slide 143
Dynamic Branch Prediction
1-bit branch predictor
2-bit branch predictor

## Slide 144
Branch Prediction Example
addi s1, zero, 0 # s1 = sum
addi s0, zero, 0 # s0 = i
addi t0, zero, 10 # t0 = 10
For: # for (i=0; i<10; i=i+1)
bge s0, t0, Done
add s1, s1, s0 # sum = sum + i
addi s0, s0, 1 # i = i + 1
j For
Done:

## Slide 145
1-Bit Branch Predictor
Remembers whether branch was taken the last time and does the same thing
Mispredicts first and last branch of loop
addi s1, zero, 0 # s1 = sum
addi s0, zero, 0 # s0 = i
addi t0, zero, 10 # t0 = 10
For: # for (i=0; i<10; i=i+1)
bge s0, t0, Done
add s1, s1, s0 # sum = sum + i
addi s0, s0, 1 # i = i + 1
j For
Done:

## Slide 146
2-Bit Branch Predictor
Only mispredicts last branch of loop
addi s1, zero, 0 # s1 = sum
addi s0, zero, 0 # s0 = i
addi t0, zero, 10 # t0 = 10
For: # for (i=0; i<10; i=i+1)
bge s0, t0, Done
add s1, s1, s0 # sum = sum + i
addi s0, s0, 1 # i = i + 1
j For
Done:

## Slide 147
Chapter 7: Microarchitecture
Superscalar & Out of Order Processors

## Slide 148
Superscalar Processors
Multiple copies of datapath execute multiple instructions at once
Dependencies make it tricky to issue multiple instructions at once

## Slide 149
Superscalar Example
Ideal IPC: 2
Actual IPC: 2

## Slide 150
Superscalar with Dependencies
Ideal IPC: 2
Actual IPC: 6/5 = 1.2

## Slide 151
Out of Order (OOO) Processor
Looks ahead across multiple instructions
Issues as many instructions as possible at once
Issues instructions out of order (as long as no dependencies)
Dependencies:
  RAW (read after write): one instruction writes, later instruction reads a register
  WAR (write after read): one instruction reads, later instruction writes a register
  WAW (write after write): one instruction writes, later instruction writes a register

## Slide 152
Out of Order (OOO) Processor
Instruction level parallelism (ILP): number of instruction that can be issued simultaneously (average < 3)
Scoreboard: table that keeps track of:
  Instructions waiting to issue
  Available functional units
  Dependencies

## Slide 153
Out of Order Processor Example
Ideal IPC: 2
Actual IPC: 6/4 = 1.5

## Slide 154
Register Renaming
Ideal IPC: 2
Actual IPC: 6/3 = 2

## Slide 155
SIMD
Single Instruction Multiple Data (SIMD)
  Single instruction acts on multiple pieces of data at once
  Common application: graphics
  Can apply to short arithmetic operations (also called packed arithmetic)
For example, add eight 8-bit elements

## Slide 156
Chapter 7: Microarchitecture
Multithreading & Multiprocessors

## Slide 157
Advanced Architecture Techniques
Multithreading
  Wordprocessor: thread for typing, spell checking, printing
Multiprocessors
  Multiple processors (cores) on a single chip

## Slide 158
Threading: Definitions
Process: program running on a computer
  Multiple processes can run at once: e.g., surfing Web, playing music, writing a paper
Thread: part of a program
  Each process has multiple threads: e.g., a word processor may have threads for typing, spell checking, printing

## Slide 159
Threads in a Conventional Processor
Single-core system:
One thread runs at once
When one thread stalls (for example, waiting for memory):
  Architectural state of that thread stored
  Architectural state of waiting thread loaded into processor and it runs
  Called context switching
Appears to user like all threads running simultaneously

## Slide 160
Multithreading
Multiple copies of architectural state
Multiple threads active at once:
  When one thread stalls, another runs immediately
  If one thread can’t keep all execution units busy, another thread can use them
Does not increase instruction-level parallelism (ILP) of single thread, but increases throughput
Intel calls this “hyperthreading”

## Slide 161
Multiprocessors
Multiple processors (cores) with a method of communication between them
Types:
  Homogeneous: multiple cores with shared main memory
  Heterogeneous: separate cores for different tasks (for example, DSP and CPU in cell phone)
  Clusters: each core has own memory system

## Slide 162
Digital Design and Computer Architecture Lecture Notes
© 2021 Sarah Harris and David Harris
These notes may be used and modified for educational and/or non-commercial purposes so long as the source is attributed.
About these Notes